The Fiber Bragg Grating (FBG) sensors are used to sense strains and temperature variation in a optical fiber. This is done by reflecting part of an input light so that a light of different wavelength is transmitted. The reflected light has a specific wavelength called Bragg wavelength (λB), the alteration of this wavelength depends on external alteration of mechanical strain or temperature.
These sensors can then be used to reconstruct the 3D shape of a flexible catheter by placing them along an optical fiber which contains four cores, in which one of these is placed in the center axis.

Assuming no variation in temperature, the shift of the Bragg wavelength depends only on the longitudinal strain of each fiber.
Using these strain values we can then compute the curvature k and his orientation φ for every sensor location si.