## Slide 1
Pagina 1
Pagina 1
  Modeling of a Flexible Probe in the V-REP environment
  A.A. 2019/20
Stefano De Filippis Riccardo Gozzovelli
Mario Vetrini Francesco Caputo
Notes: 1

## Slide 2
Page 2
ROBOTIC SURGERY, A NEW ERA...
29/04/2020
Enhanced dexterity.
Increased accuracy.
Lower chance of complications.
Easier recovery.

## Slide 3
Page 3
… WITH STILL SOME PROBLEMS
29/04/2020
0.1mm - 10mm
1mm - 15mm
5µm - 10µm
Training.
Lack of sensory feedback (tactile and force).
Size.
Malfunctioning.

## Slide 4
Page 4
ENDOVASCULAR CATHETERS
29/04/2020
Sensei X
Hansen Magellan
Artisan Extend

## Slide 5
Page 5
MODEL OF A FLEXIBLE PROBE
29/04/2020
KINEMATIC STRUCTURE:
Single rigid body
Chain of elastic links
Chain of rigid links
Different approaches for:
FORCE ESTIMATION:
Curvature + Cosserat rod model
FBG sensors

## Slide 6
Page 6
CONTACT FORCES COMPUTATION
29/04/2020
Single torque component
i-th flexural stifness
i-th bending amount
Torque vector
contact point Jacobian
external wrench
Invert
Invert
Single contact point
Multiple contact points

## Slide 7
Page 7
V-REP ENVIRONMENT
29/04/2020
3-D simulation software.
Version used 3.6.2.
Many problem to overcome:
- missing material properties;
- search for the best combination of links and joints;
- tweaking of internal parameters ;

## Slide 8
Page 8
FLEXIBLE PROBE - COMPONENTS
29/04/2020
1. Links
Non-dynamic
Great variety of shape
32 links divided into:
Link n.1 connected to the base.
Link n.2 to Link n.31 attached one after the other.
Link n.32 tip of the probe.
Simulation problems!
34 cm long

## Slide 9
Page 9
FLEXIBLE PROBE - COMPONENTS
29/04/2020
2. Joints
Dynamic.
Used to build the chain structure.
Three types of interest.
Different behavioural properties.
Controllable in different ways.
Revolute
Prismatic
Shperic

## Slide 10
Page 10
FLEXIBLE PROBE - COMPONENTS
29/04/2020
2.1 Joints elasticity
Control joints via a PID controller
TORQUE DUE TO THE CONTROL MODE
Set derivative and integral gain to 0
Choose kp and τmax such that
At rest qd=0, so
SPRING DAMPED control mode

## Slide 11
Page 11
FLEXIBLE PROBE - SETTINGS
29/04/2020
2 DOFs case
1 DOF case

## Slide 12
Page 12
FLEXIBLE PROBE - SETTINGS
29/04/2020
2 DOFs case​
 | GRAVITY ON | GRAVITY OFF
PASSIVE JOINTS | X | 
ACTIVE JOINTS |  | 

## Slide 13
Page 13
FLEXIBLE PROBE - SETTINGS
29/04/2020
2 DOFs case​
 | GRAVITY ON | GRAVITY OFF
PASSIVE JOINTS |  | X
ACTIVE JOINTS |  | 

## Slide 14
Page 12
FLEXIBLE PROBE - SETTINGS
29/04/2020
2 DOFs case​
 | GRAVITY ON | GRAVITY OFF
PASSIVE JOINTS |  | 
ACTIVE JOINTS | X | 

## Slide 15
Page 15
FLEXIBLE PROBE - SETTINGS
29/04/2020
2 DOFs case​
 | GRAVITY ON | GRAVITY OFF
PASSIVE JOINTS |  | 
ACTIVE JOINTS |  | X

## Slide 16
Page 16
FLEXIBLE PROBE - SETTINGS
29/04/2020
1 DOF case​
 | GRAVITY ON | GRAVITY OFF
PASSIVE JOINTS | X | 
ACTIVE JOINTS |  | 

## Slide 17
Page 17
FLEXIBLE PROBE - SETTINGS
29/04/2020
1 DOF case​
 | GRAVITY ON | GRAVITY OFF
PASSIVE JOINTS |  | X
ACTIVE JOINTS |  | 

## Slide 18
Page 18
FLEXIBLE PROBE - SETTINGS
29/04/2020
1 DOF case​
 | GRAVITY ON | GRAVITY OFF
PASSIVE JOINTS |  | 
ACTIVE JOINTS | X | 

## Slide 19
Page 19
FLEXIBLE PROBE - SETTINGS
29/04/2020
1 DOF case​
 | GRAVITY ON | GRAVITY OFF
PASSIVE JOINTS |  | 
ACTIVE JOINTS |  | X

## Slide 20
Page 20
FLEXIBLE PROBE - EXPERIMENTS
29/04/2020
Model validation
Spring Damper mode
Force sensor
Three experiments:
Single force at the tip
Three forces along the structure
Six forces along the structure

## Slide 21
Page 21
EXPERIMENT STEPS
29/04/2020
Apply forces on some links;
collect at each instant torque, joints and force measurements;
pass the measurements to Matlab;
compute the contact Jacobian at each instant;
filter joint and torque measurements;
estimate forces;
smooth estimated forces;

## Slide 22
Page 22
EXPERIMENT 1 - SINGLE FORCE
29/04/2020
Constant force produces wrong behaviour.
Use of a linearly increasing and decreasing force.

## Slide 23
Page 23
EXPERIMENT 2 – THREE FORCES
29/04/2020
Same type of force as before.
Force produced by a collision with a world object.
Contact points along the probe are known (link 27,28,29).

## Slide 24
Page 24
EXPERIMENT 3 – SIX FORCES
29/04/2020
Identical to the previous case but with three additional contact points (7,8,9,10,25,26).

## Slide 25
Page 25
CONCLUSIONS
29/04/2020
Challenges in reproducing the dynamic properties of a flexible probe.
V-REP fails to handle a large number of small size objects attached one to another.
Prominent oscillations are produced together with lots of vibrations.
This effect amplifies as more DOFs are addressed.
Elastic effect of materials can be reproduced through "specific" control laws.
The proposed estimation method is more accurate on the Y direction than on the X direction.